Swyx driver package for SX2 ISDN boards

Content

1. Version History

2. Installation

3. Driver update

1. Version History

6.20.0.7

Added: Fixed issues observed by quality assurance

6.20.0.6

Added: Fixed issues observed by quality assurance

6.20.0.5

Added: Fixed issues observed by quality assurance

6.20.0.4

Added: Production SX2-express SinglePRI board fully supported

6.20.0.3

Added: Production SX2-express DualPRI board fully supported

6.20.0.2

Added: BRI synchronization source selectable via GUI

6.20.0.1

Initial version with support for prototype SX2-express DualPRI

2. Installation

After a re-boot the SX2 boards are automatically detected by the hardware wizard. This software starts the ISDN wizard (part of the Windows system) and the installation will start. To install the driver software for the SX2 adapter simply follow the steps displayed on the screen.

If you want to configure the adapter (concerning the D-Channel protocol), go to 'My Computer' icon on your desktop, click the right mouse button and activate 'Properties', click to 'Hardware' and start 'DeviceManager': Under 'Network adapters' you will find in here your installed SX2 adapter. Go to this entry and click again the right mouse button and start 'Properties'. On 'Advanced' and 'ISDN' you will find the places to take the SX2 adapter configuration.

For more details see the manual or KB-article kb3159.

3. Driver Update

If you want to update the installed driver please proceed as follows:

Go to the Hardware tab of the "System Properties" dialog of  Windows, click on "Device Manager" and

select the installed SX2 ISDN card. Click the right mouse button and choose "Uninstall...".  After the

current driver is deinstalled click the button “Hardware Wizard..." on the Hardware tab. The ISDN adapter will be found by this routine and you have to specify the path where the new driver is located.

After this follow the procedure as described in chapter 1.

If recommended in this document you should update the SX2 WAN miniport driver.

Important: The update is not done during update of the ISDN driver. You need to update the SX2 WAN miniport driver via the device manager. By default the SX2 WAN miniport driver is hidden in the device manager GUI. You need to enable "show hidden devices" in the device manager menu. Then you see the SX2 WAN miniport and can proceed with the update like usual.