Swyx driver package for SX2 ISDN boards

Content

1. Version History

2. Installation

3. Driver update

1. Version History

8.0.0.15

Important: 	In case of an update don't forget to update the SX2 WAN Miniport driver

if it is enabled.
	Fixed: #10762: only 29 channels can be allocated on a SX2 PRI board

8.0.0.14

Modified: Tracing of cancelled I/O operations

8.0.0.13

Fixed: #9743: SX2-express DualPRI: ISDN Driver triggers watchdog during system reboot

8.0.0.12

Fixed: #9668: ISDN SX2 driver: driver signals 'any' b-channel in setup, which leads to a 						  failed call

Fixed: #9683: SX2 ISDN Driver extracts only one Progress IE from any D-Channel 								  message

8.0.0.11

Fixed: #9414: driver should truncate oversized DisplayIE within SETUP message 								  instead of rejecting whole call

8.0.0.10

Modified: Added tracing of internal event allocations

8.0.0.9

Modified: Online Help removed from Setup.

ISDN driver Help is part of the Administration documentation.

8.0.0.8

Modified: WAN Miniport is disabled per default

See “Properties -> Advanced -> ISDN Parameters -> ISDN Card ID”

8.0.0.7

Modified: Setting framing format of SX2-express PRI to CRC4 and DoubleFrame

8.0.0.6

Fixed: #6870: CCNR related messages are not correctly associated to CAPI calls

Fixed: #6872: SX2 ISDN Driver: sometimes 100% cpu load with SinglePRI-express board

8.0.0.5

Fixed: #6121: DTMF key generation in ISDN driver differs from mechanism in SwyxIt!

Modified: Decreased volume of DTMF digits

8.0.0.4

Fixed: #5531: Generation of DTMF digits blocks media streaming

8.0.0.3

Modified: Not marking SX2 WAN Miniport as Removable

8.0.0.1

Fixed: Passed Microsoft driver test suite

7.0.0.53

Fixed: Supporting Non CRC-4 modus on SX2 PRI/DualPRI cards (not PCI-express cards)

7.0.0.52

Fixed: #4672: ISDN Driver may crash on sending of DTMF digits

7.0.0.51

Ticket 100707-29606:	Not sending TA_TEIVERIFYREQ in NT mode

(this is not a crucial change but may confuse any problem analysis)

7.0.0.50

Modified:   Showing ISDN Card ID in the SX2 adapter configuration

Modified:	  Automatic PCM clock configuration

Modified:	  D-Channel processing on SX2-express PRI/DualPRI cards

7.0.0.49

Fixed: #4220: Primary PCI-express: Sometimes voice connections switched via PCM cable 					  	  are distorted

Fixed: #3768: Clock synchronization not correctly set on SX2-express DualPRI if the 							  	  second port is clock master

Removed:	  Manual selection of PCM clock source

7.0.0.48

Fixed: #3772: No outgoing calls on ISDN BRI interface

7.0.0.47

Fixed: #4195: D-Channel Restart message disconnects all running connections

7.0.0.46

Fixed: #3926: Primary PCI-express: Sometimes D-Channel messages get lost

7.0.0.44

Fixed: #3616: ISDN Driver may crash the operating system if an application doesn't 							  	  consume CAPI messages

Fixed: #Swyx23813: permanent layer 2 switched off changing from PtP to PmP mode

7.0.0.41

Important: 	In case of an update don't forget to update the SX2 WAN Miniport driver.
					Otherwise your system may crash.

One installation package for x86 and x64 platforms.

Supporting Server 2008 and Server 2008 R2.

Fixed: Data protocols (HDLC and X.75) are fully supported now.

Fixed: Several complaints of the driver verifier.

Added: Packet Loss Info.

Added: PCM Switching support.

Added: GlobalLogger trace session.

7.0.0.0

Initial version with new internal redesign.
	Data protocols (HDLC and X.75) are not fully supported yet.

2. Installation

After a re-boot the SX2 boards are automatically detected by the hardware wizard. This software starts the ISDN wizard (part of the Windows system) and the installation will start. To install the driver software for the SX2 adapter simply follow the steps displayed on the screen.

If you want to configure the adapter (concerning the D-Channel protocol), go to 'My Computer' icon on your desktop, click the right mouse button and activate 'Properties', click to 'Hardware' and start 'DeviceManager': Under 'Network adapters' you will find in here your installed SX2 adapter. Go to this entry and click again the right mouse button and start 'Properties'. On 'Advanced' and 'ISDN' you will find the places to take the SX2 adapter configuration.

For more details see the manual or KB-article kb3159.

3. Driver Update

If you want to update the installed driver please proceed as follows:

Go to the Hardware tab of the "System Properties" dialog of  Windows, click on "Device Manager" and

select the installed SX2 ISDN card. Click the right mouse button and choose "Uninstall...".  After the

current driver is deinstalled click the button “Hardware Wizard..." on the Hardware tab. The ISDN adapter will be found by this routine and you have to specify the path where the new driver is located.

After this follow the procedure as described in chapter 1.

If recommended in this document you should update the SX2 WAN miniport driver.

Important: The update is not done during update of the ISDN driver. You need to update the SX2 WAN miniport driver via the device manager. By default the SX2 WAN miniport driver is hidden in the device manager GUI. You need to enable "show hidden devices" in the device manager menu. Then you see the SX2 WAN miniport and can proceed with the update like usual.